## Slide 1
About Hardware Optimization in Midas SW
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 2
How many cores of CPU does Midas SW support?
Q1.
A1] 8 cores
Midas support up to 8 cores. (It is recommended to be used in multiples of 2 like 2, 4, 8 )
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 3
Tip1]
Multi Frontal Sparse Gaussian(ON) & Multi Processer(OFF)
 Automatically, useable maximum number of multi core are working.
Multi Frontal Sparse Gaussian(ON) & Multi Processer(ON + number)
 It will work for the number entered.
The analysis speed is faster when there are many cores.
but It can not have much effect on more than 4 cores.

## Slide 4
Is Midas SW supporting GPU acceleration?
Q2.
A2] Yes, Midas SW is supporting GPU acceleration
But it supports only GPU of Tesla.
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 5
Tip2]
We must have at least two cards with GPU. One is for display, and the other is for computing. The GPU card for computing must be a card of Tesla series.
The causes and Error messages by GPU ;
- If you do not have a GPU card
 GPU ACCELERATION: DISABLED (NO GPU)
- If your GPU is not Nvidia GPU
 GPU ACCELERATION: DISABLED (NO CUDA SUPPORTING GPU)
- For older GPU
 GPU ACCELERATION: DISABLED (LOW COMPUTE CAPABILITY)
- If there is one GPU or is not a Tesla series
 GPU ACCELERATION: DISABLED (MORE THAN TWO GPU'S REQUIRED)

## Slide 6
Tip2] (continue)
For reference, we can expect the effect by GPU in a large model with at least a few hundred thousand degrees of freedom, so I think it is unnecessary to use the GPU in general structural analysis.
If you want to know information for the available GPU
Please refer to the next web page.
https://en.wikipedia.org/wiki/Nvidia_Tesla
And GPU cards are very expensive. Therefore, if you want to improve the analysis speed, I recommend that you consider upgrading memory or CPU than GPU.

## Slide 7
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 8
How much memory does the Midas SW support under 64bit system?
Q3.
A3] 16G
Even when the memory is very large, only 16G is used as the maximum system memory,
and about 70% of 16G are used for the analysis process.
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 9
How much memory does the Midas SW support under 32bit system?
Q3. (sub question)
A3] 1.44G
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 10
How much memory does user’s PC need to use 16G?
Q3. (sub question)
A4] 24G (24G * 70% = 16G)
The maximum available memory size is the smallest value in 70% of RAM and 16 GByte.
Notes: I will take time to learn about the hardware that can be used to make the MIDAS program useful.

## Slide 11
Tip3]
As everyone know, large memory can reduce computing time.
But the effect of CPU, main board, memory type, and HDD buffer size may be more important than memory size.